## Slide 1: Assignment 2
Task 1 - Implementation as a Group and Demonstrate

## Slide 2: Team Formation – Members and Roles
Charlie Williams (2235685) – Network Administrator
Jonathan Morgan (2218940) – Network Administrator

## Slide 3: Communication Methods
WhatsApp
Email
Face to face communication
Microsoft Teams

## Slide 4: Objectives
Build basic IP networking setup with 7 devices and routing
Configure working SSH on Cisco devices
Build Linux VM with working Ansible install
Ansible working via SSH to the 4 Cisco networking devices
Ansible runs ‘Playbooks’ to automate further configuration of the 4 Cisco networking devices
Deliver demonstration – 7th January 2025

## Slide 5: Planning
Option 1 – Use tools to automate configuring network devices
Reasons:
  We both preferred the idea of working with Cisco networking devices over writing a python app that used REST API’s.
  Using physical devices in the LAB – slightly trickier as can only work whilst ‘on-site’ but provides a more ‘realistic’ experience to learn from
  Using Ansible as the primary tool to enable automation – it was the tool taught during lectures, but also seeing widespread real-world usage
  Automations to achieve would ideally be information gathering, security stance setting and routing protocol configuration

## Slide 6: Basic Topology
LAN3 | 
R1 Serial 0/1/0 | 10.0.0.1/30
R2 Serial 0/1/0 | 10.0.0.2/30
LAN1 | 
R1 Gig 0/0/0 | 192.168.1.1/24
SW1 SVI | 192.168.1.2/24
PC1 | 192.168.1.3/24
AnsibleVM on PC1 | 192.168.1.4/24
LAN2 | 
R2 Gig 0/0/0 | 192.168.100.1/24
SW2 SVI | 192.168.100.2/24
PC2 | 192.168.100.3/24

## Slide 7: Why Ansible for network automation?
As previously mentioned, Ansible is what was taught during lectures.
Ansible uses SSH to communicate with devices, so no need for an installed agent on recipient machines. Works well for this scenario [1]
Ansible uses YAML, which is human readable. This means it would be easier for us to learn and understand. [2]
[1]: https://ezeelive.com/ansible-advantages-disadvantages
[2]: https://orhanergun.net/introduction-to-ansible-for-network-automation

## Slide 8: Projected Timeline
https://www.onlinegantt.com/ used to generate our Gantt chart

## Slide 9: GitHub
A ‘private’ repository exists at:
https://github.com/2wheelsdown/NPAssignment2